## Slide 1: Overcoming Throughput Degradation in Multi-Radio Cognitive Radio Networks
M.Sc. Thesis Proposal
by
Tanvir Ahmed Khan
Student ID: 1014052013
Supervised by:
A. B. M. Alim Al Islam, Assistant Professor.
Dept. of CSE, BUET.

## Slide 2: Background of Our Study
Licensed frequency spectrums are mostly under-utilized! [8]

## Slide 3: Background of Our Study
How to increase the spectrum utilization?

## Slide 4: Cognitive Radio Networks (CRNs)
  Comprises of two different types of users
Primary users
(licensed)
Secondary users
(unlicensed)

## Slide 5: Cognitive Radio Networks (CRNs)
Primary users
(licensed)
Secondary users
(unlicensed)
  Comprises of two different types of users

## Slide 6: Cognitive Radio Networks (CRNs)
Primary users
(licensed)
Secondary users
(unlicensed)
  Comprises of two different types of users

## Slide 7: Cognitive Radio Networks (CRNs)
Primary users
(licensed)
Secondary users
(unlicensed)
  Comprises of two different types of users

## Slide 8: Applications of Cognitive Radio Networks
CRN Applications
High-Speed Rural Internet
Military Networks
Emergency Networks
Multimedia

## Slide 9: Multi-radio Networks
Improves network capacity [2, 3]
user

## Slide 10: Multi-radio Networks
Enhances transmission reliability [6]
user

## Slide 11: Multi-radio Networks
  Enables heterogeneous wireless access [7]
user

## Slide 12: Multi-radio Cognitive Radio Networks
Secondary user
Secondary user

## Slide 13: Motivation Behind Our Work
Throughput degradation in multi-radio CRNs

## Slide 14: Motivation Behind Our Work
Throughput degradation in multi-radio CRNs
  at the benefit of delay improvement [4]

## Slide 15: Our Research Problem
How to overcome this throughput degradation in multi-radio CRNs?

## Slide 16: Related Research Work
Ahmadi et al., Vehicular Technology Conference (VTC) Fall, 2012 [1]
  Solves the channel assignment problem for the single receiver radio
  Considers only two sender radios
  Does not investigate the performance of the network varying the number of radios

## Slide 17: Related Research Work [contd.]
Zhong et al., Wireless Personal Communications (WPC), 2014 [9]
  Presents a channel assignment algorithm for multi-radio cognitive radio network
  While assigning channels among available radios only channels are ranked
    Does not consider conditions of radio
  No analysis on throughput with an increase in number of radios

## Slide 18: Related Research Work [contd.]
Li et al., ACM MSWiM, 2014 [5]
  Presents a rendezvous channel establishment algorithm for multi-radio cognitive radio networks
  Shows that maximum time to rendezvous reduces with an increase in number of radios
  However, does not provide any approach on how these radios will be used for data transmission

## Slide 19: Related Research Work [contd.]
Khan et al., IEEE WiMob, 2015 [4]
  Employs multiple radios for data transmission
    Shows that delay gets improved at the cost of throughput degradation with an increase in number of radios
  Does not consider intra-user radio interference in case of omnidirectional antenna

## Slide 20: Objectives & Outcomes
Propose an approach to improve throughput
  Feedback-based multi-radio exploitation approach
Propose a new approach
Feedback-based multi-radio exploitation approach

## Slide 21: Objectives & Outcomes [contd.]
Performance evaluation of our proposed approach
Topology1
Topology2
Topology3
Implementation of our proposed approach

## Slide 22: Objectives & Outcomes [contd.]
Performance comparison of our proposed approach with that of other existing approaches
Our proposed approach
Existing approaches
Ahmadi et al. [1] Khan et al. [4] Zhong et al. [9]

## Slide 23: Methodology of Our Study
Radio-channel assignment with intra-user collision avoidance

## Slide 24: Methodology of Our Study [contd.]
Radio-channel access based on radio and channel statistics
  Feedback based multi-radio exploitation
Packet
Packet
Radio
Packet
queued
Packet
transmitted
Packet
delivered
0
1
1
0
1
1
1
1
Channel
Packet
transmitted
Packet
delivered
0
1
1
1
1
0

## Slide 25: Methodology of Our Study [contd.]
Performance analysis of the proposed approach
Topology1
Topology2
Our proposed approach
Existing approaches
[1, 4, 9]

## Slide 26: Results Obtained So Far
Constant throughput degradation is no longer present

## Slide 27: Results Obtained So Far [contd.]
Constant throughput degradation is no longer present
  delay improvement is compromised slightly

## Slide 28: Conclusion
Throughput degradation in multi-radio cognitive radio networks is a well-known problem.
  We will propose a feedback-based multi-radio exploitation approach to solve the problem.
  We will evaluate the performance of our proposed approach through experimentation.
  We will compare the performance of our proposed approach with that of other contemporary approaches.

## Slide 29
Thank you!

## Slide 30: References I
Maryam Ahmadi, Yanyan Zhuang, and Jianping Pan. Distributed robust channel assignment for multi-radio cognitive radio networks. In Vehicular Technology Conference (VTC Fall), 2012 IEEE, pages 1-5. IEEE, 2012.
Paramvir Bahl, Atul Adya, Jitendra Padhye, and Alec Walman. Reconsidering wireless systems with multiple radios. ACM SIGCOMM Computer Communication Review, 34(5):39-46, 2004.
Richard Draves, Jitendra Padhye, and Brian Zill. Routing in multi-radio, multi-hop wireless mesh networks. In Proceedings of the 10th annual international conference on Mobile computing and networking, pages 114-128. ACM, 2004.
Tanvir Ahmed Khan, Chowdhury Sayeed Hyder, and ABM Islam. Towards exploiting a synergy between cognitive and multi-radio networking. In Wireless and Mobile Computing, Networking and Communications (WiMob), 2015 IEEE 11th International Conference on, pages 370-377. IEEE, 2015.
Guyue Li, Zhaoquan Gu, Xiao Lin, Haosen Pu, and Qiang-sheng Hua. Deterministic distributed rendezvous algorithms for multi-radio cognitive radio networks. In Proceedings of the 17th ACM international conference on Modeling, analysis and simulation of wireless and mobile systems, pages 313-320. ACM, 2014.

## Slide 31: References II
Allen Miu, Hari Balakrishnan, and Can Emre Koksal. Improving loss resilience with multi-radio diversity in wireless networks. In Proceedings of the 11th annual international conference on Mobile computing and networking, pages 16-30. ACM, 2005.
Wei Song and Weihua Zhuang. Performance analysis of probabilistic multipath transmission of video streaming traffic over multi-radio wireless devices. Wireless Communications, IEEE Transactions on, 11(4):1554-1564, 2012.
Vaclav Valenta, Roman Marsalek, Genevieve Baudoin, Martine Villegas, Martha Suarez, and Fabien Robert. Survey on spectrum utilization in europe: Measurements, analyses and observations. In Cognitive Radio Oriented Wireless Networks & Communications (CROWNCOM), 2010 Proceedings of the Fifth International Conference on, pages 1-5. IEEE, 2010.
Xiaoxiong Zhong, Yang Qin, and Li Li. Capacity analysis in multi-radio multi-channel cognitive radio networks: A small world perspective. Wireless Personal Communications, 79(3):2209-2225, 2014.